## Slide 1: Cellular Metering Solutions and Integration with MV-90 and Fiber
July 22, 2024
1:00 PM -- 2:30 PM
Jon Scott

## Slide 2: Adaptiv Architecture

## Slide 3: Adaptiv Benefits
Zero Infrastructure
  Easy to deploy
  No costly infrastructure to install or maintain
Billing Data Transfer
  Standards-based integration to utility billing applications
  Multispeak, MV-RS, CMEP
Solution as a Service
  Seamless Cloud Software and Support
  No IT hardware to buy or databases to manage
  Nighthawk provides all hosting and support
Secure, Reliable Reads scheduled or on demand
  Daily consumption
  Move in/move out reads
  Disconnects

## Slide 4: Adpativ Deployment Options
Full AMI
  Typically targeted at small – medium-size municipalities/cooperatives.
  Cell + Mesh
  Multi-service
    Full two-way AMI for electric or electric + water (no water-only).
    Gas remote reading is handled through ERT collection using our ERT Collector Hub Meters. NOT full two-way AMI for Gas.
Gap Fill
  Typically targeted at larger utilities to fill in gaps in existing AMI systems.
Tactical/Targeted Solutions
  Used for targeted applications like remote disconnect, remote reading, Christmas Lights, crypto-mining, etc.
  When dealing with a utility, can naturally grow into a full AMI system.
ERT Collection
  For electric and water customers, can be used as a bridge to Full two-way AMI.
  Rarely do we reliably collect ALL electric, water and gas ERT signals.

## Slide 5: Adaptiv Endpoints
Device Type | Cellular + RF Mesh HUB | ERT Reader Cell+Mesh HUB | RF Mesh only LEAF | Disconnect option
Aclara kV2c |  | --- | --- | ---
Aclara I-210+c |  | --- |  | 
Itron Centron II |  |  | --- | 
Water End Point | --- | --- |  | ---
All Adaptiv devices contain a 2.4GHz RF Mesh transceiver connecting all devices, including HUBS
Cellular Hubs manage multiple LEAF devices
Population diversity: ~10% HUB to 90% LEAF
Electric meters available in all S Base form factors and classes

## Slide 6
ADAPTIV™ | ONE HUB TO MANY LEAFS
    Scalable, self-healing, self-configuring RF Mesh network
    High bandwidth LTE cellular-mesh
      One HUB per cluster of 10 -20 LEAF devices – electric and water
      LEAF devices provide up to 4 hops to maximize coverage
    Built-in security and redundancy
    Water interval data and leak detection with exceptional battery life
    Simple installation and maintenance
Cellular LTE
2.4 GHz RF Mesh

## Slide 7: What does this have to do with Fiber?

## Slide 8: Fiber Hub Intro
Introducing late 4th quarter 2023
The Nighthawk Ethernet HUB product is a self-contained mesh HUB device with a wired Ethernet uplink.
  Fiber hub is Adaptiv compatible – uses same Synapse mesh module
  Acts as a collector for multiple devices
  Technically an infrastructure device
“Fiber” is used because the initial product offering has been designed to work with customer deployed PON networks
  With further development, network uplink could be connected to any copper Ethernet interface
  Circuitry included to support cellular based version (replaces PON) – reduces operating costs (less cellular outtakes)
Customer assisted testing and validation ongoing
LED Status Indicators
2.4GHz Mesh Antenna

## Slide 9
ADAPTIV™ | ONE HUB TO MANY LEAFS
    Scalable, self-healing, self-configuring RF Mesh network
    Utilize High bandwidth Fiber backhaul
      One HUB per cluster of greater than 20 LEAF devices – electric and water
      LEAF devices provide up to 4 hops to maximize coverage
    Built-in security and redundancy
    Water interval data and leak detection with exceptional battery life
    Simple installation and maintenance
Fiber Hub
Fiber Network
2.4 GHz RF Mesh

## Slide 10: Fiber Hub Use Cases
Ideal for utilities who have mostly fiber throughout service territory
  Federal government incentivizing rural coop fiber to the home
  Utilities looking for applications to use the deployed fiber
Allows for network performance tuning
  Mounting on a pole improves device connectivity – increased RF range
  Allow stranded devices network access
To be confirmed in validation testing:
  Connect > 20 devices via mesh
  Height is our friend
  Standard hub averages up to 10-20 leaf devices
  Maximum hub capacity 150 leafs

## Slide 11: Fiber Hub Features
120/240 VAC power input
  Locking power cord
Size: 7” x 6” x 2.5”
  Wall or Pole mounting
Operating Temp: -20C / +65C
External I/O’s:
  12 VDC output for downstream devices (optional)
  RJ-45 sealed connector – 100Base-TX
  USB-C sealed Terminal Access Port for configuration, diagnostics, and Synapse script upgrades
LED Status Indicators for power, network uplink, and alarm status
Microprocessor based to support multiple peripherals
  ST Micro STM32F767ZIT6
  Processor firmware OTA upgradable
Wall mount Brackets
2.4GHz Mesh Antenna
LED Status Indicators

## Slide 12: Fiber Hub Features – con’t
Advanced Outage Management power fail detection
  Configurable blink and sustained outage event thresholds, event logging and data upload
Rechargeable Battery Backup of 10 minutes to allow for last gasp transmissions
  Powers internal circuitry only
Supports OTA firmware upgrades to associated mesh devices
Robust end to end security and encryption

## Slide 13: DirectConnect
Compatible with all data acquisition software that supports TCP/IP connections

## Slide 14: DirectConnect Solution
Introducing Nighthawk DirectConnect TCP/IP connectivity on the Aclara kV2c mid second quarter 2023
  Connects directly to the meter’s C12.19 data structure
Connects directly with Itron MV-90, Aclara MeterMate, Trilliant PrimeRead, or Trilliant UnitySuite data acquisition software
Robust, secure, and efficient bidirectional message delivery mechanism
Utilizes same proven LTE hardware as Adaptiv HUB solutions (less RF mesh module)
  Cellular devices only – not compatible with Leaf (mesh) meters
In final testing now
  Full data retrieval
  Features such as last gasp, modem configuration and firmware update supported
  Can use MeterMate to update meter firmware and configuration
  Compatible with Nighthawk kV2c meters – full meter functions supported
    Itron Poly to follow late 2023/early 2024
  Currently supported on Verizon or AT&T
14

## Slide 15: DirectConnect Solution
Does not require any middleware
  Stand alone solution that does not require Adaptiv HES or other Adaptiv endpoints
No recurring fees from Nighthawk. Utilize existing utility private contract with AT&T or Verizon
  Customer provides SIMs
  Other carriers can be supported
    Other carriers can be supported with purchase commitments
    Requires testing and certification
Warranty Term: 1 year

## Slide 16: Module Specifications
connectivity | AT&T or Verizon LTE cellular
security | ANSI C12.22 128-bit AES/EAX’ (combined encryption/authentication)
memory | 40 kB
clock synch | to LTE network
firmware | over-the-air upgradable
power outage & restoration reporting | aggregated real-time reporting
DirectConnect Functionality
protocols | TCP/IP
modulation | OFDM (Orthogonal Frequency Division Multiplex)
data rate | LTE Cat-1 (5 Mbps ↑, 10 Mbps ↓ )
frequency band | LTE Bands 2, 4, and 12 or 13
transmit EIRP | +20 dBm (including antenna gain)
sensitivity | -103 dBm (@ 1% PER; incl. antenna gain)
Radio Performance
burden (including module) | 120 V: 1.3 W 240 V: 1.6 W | 277 V: 1.7 W 480 V: 2.4 W
S-Base | 6.95”/17.65 cm (diam). x 4.38”/11.11 cm (D) 4 lbs / 1.8 kg net | 
temperature | -22° F / -30° C to +158°F / +70° C | 
humidity | 5 to 95% non-condensing | 
Power, Physical, & Environmental
radio emissions | FCC Part 15 Class A Industry Canada ICES-003 Class A | 
device IDs | FCC ID: RI7LE910NAV2 IC ID: 5131A-LE910NAV2 | 
safety | ANSI C37.90.1 ANSI C62.41 | 
metrology | ANSI C12.1 ANSI C12.18 ANSI C12.19 | ANSI C12.20 ANSI C12.21
Compliance

## Slide 17: Simple Configuration

## Slide 18: Questions and Discussion
Jon Scott
TESCO NIGHTHAWK Sales Manager
TESCO – The Eastern Specialty Company
Bristol, PA
404.451.8444
This presentation can also be found under Meter Conferences and Schools on the TESCO website: tescometering.com
ISO 9001:2015 Certified Quality Company
ISO 17025:2017 Accredited Laboratory