## Slide 1: ROUNDTABLE: - Tracking Failure Curves of Early AMI Deployments - Considerations for AMI 2.0 - System Obsolescence Considerations
July 24, 2024
8:45 AM -- 10:15 AM
Glenn Pritchard

## Slide 2: Ice Breaker
Introductions
  What company are you representing and what is your role?
  Describe your AMI deployment and when was it installed?

## Slide 3: PECO’s AMI Deployment

## Slide 4: AMI at PECO
PECO is located in Southeastern Pennsylvania, serving Philadelphia and the surrounding counties
PECO installed a Sensus FlexNet AMI platform from 2011-2016
The system serves:
  1.725M electric meters
  550k gas meters
  4,200+ Distribution Automation devices (Reclosers, Capacitors, FCI’s, etc)
Initial goals of the AMI deployment included:
  Meeting Pa. Act 129 of 2008 required meter functionality, including
    Hourly interval data (15 minute or faster as needed)
    Remote disconnect & connect
    Outage Alarming
  Meeting and exceeding performance levels of the existing Ladis+Gyr CellNet AMR system
  Creating opportunities to expand and deliver enhanced functions that leverage the network and meters

## Slide 5: AMI Background

## Slide 6: Meter Obsolescense

## Slide 7: Meter Lifecycle
New Smart Meters have a finite useful life (15-20yrs)
It is important to recognize that there will be a future need to replace both the meters and the networks
Is a future full redeployment an option?
What about a future annual replacement plan?
It pays to plan for this now, account for it in your Long-Range Financial Plans
It is also advisable to include your regulators and stakeholders

## Slide 8: Projected Meter Failures
Analysis of failure rates over the past 3 years confirms current failure rate curve projections
Recommend beginning replacement in earnest by 2027 to stay ahead of the expected failure rates
Meter failure rates will quickly increase by 2029, exceeding meter shop capacity to adequately respond without significant additional support
  ~50% deployment needed by 2031 to stay ahead of failure curve
Notes: Southern Cal Edison currently has a 2% failure rate in their meters (1/3 due to corroded batteries and 2/3 due to other issues).
  By 2028 the rate is expected to increase to 80%.
  Current meter population is 5.2M meters
  Replacement Plan will be funded through their Utility Commission (5-6 year Plan starting in 2028 costing $2.5B-$3B). Plan will also include the cost of a communication system upgrade (Silver Springs Network or new system)

## Slide 9: Impacts from the Pandemic
How did COVID change AMI?
Material Supply Constraints
Premature Material Obsolescence
Technology Evolution
New Customer Expectations

## Slide 10: AMI 2.0?

## Slide 11: AMI 2.0
What is AMI 2.0?
What is changing?

## Slide 12: AMI 2.0
AMI 2.0 is a system upgrade that results in increased network reliability and more reliable exchanges of data
The functions build upon AMI 1.0, which set the foundation for the future
“Many of the end user/customer advantages promised by AMI 1.0 did not materialize.”

## Slide 13: More Data & New Functions
Increased Sample Rates
  60-, 15-, 5- & 1-minute samples are possible
Multiple Recording Channels
  Some vendors are claiming up to 32 independent channels are available
Distributed Intelligence and Decision Making local to the meter
Question – Has the network and head-end kept pace with the new meter capabilities?

## Slide 14: New Functions
On-Board Decision Making
  EV Management
  Voltage Regulation
Analytics
  Non-intrusive load monitoring & Load Disaggregation
New Communications Methods for FAN and HAN
  WiFi Enabled Meters

## Slide 15: AMI 2.0 Use Cases
AMI – Advanced Analytics Opportunities - Utility Analytics Institute

## Slide 16
From Deloitte’s AMI 2.0 Study
https://www2.deloitte.com/us/en/pages/energy-and-resources/articles/next-gen-advanced-metering-infrastructure.html

## Slide 17: Distributed Intelligence
Recently, several meter manufacturers have begun to develop Distributed Intelligent models and applications for their AMI meters
This is seen as a new means to add future functions to the meters
The concept mimics the “Apple iStore” concept where apps are available to be downloaded into meters as needed
Apps are often targeted on Real-Time decision making and control solutions
DI is often associated with Mesh Network based systems where latency in communications may be a factor

## Slide 18: Distributed Intelligence
Sample Use Cases:
Hot Socket Monitoring & Action
Smart Inverter Interface – Autonomous control
Solar and Battery Support – Load Coordination
Power Quality Analysis

## Slide 19: Alternative Perspectives

## Slide 20: Sensus FlexNet V2 – “Crowded Highways Presentation”*
* - Full slides in Appendix
The FlexNet V2 Protocol enable more efficient use of the RF Channels, delivering higher speed, higher capacity and more secure communications

## Slide 21: Sensus V2 Protocol
What is V2?
  The V2 protocol is a new method to communicate to our meters
  It easily coexists with the legacy V1 protocol, using the same RF spectrum
  V2 is built upon higher speed messages and more efficient data packets
Why do we need it?
  Performance Improvements
  Improved Security
  Enables new functionality on NextGeneration Electric and Gas Meters
When is V2 available?
  NOW, All eligible transceivers are configured to support V2 communications
Do we have any devices on the V2 Protocol?
  YES, more than 25,000 meters using the V2 Protocol today

## Slide 22: What is a NextGen Meter?
Communications
V2 – More efficient utilization of infrastructure leading to higher capacity and speed
Security / Encryption – mandatory, enhanced security measures
New Network hardware – improved software and contemporary hardware
Functionality
Multiple Independent Channels – beyond usage, including voltage, power quality, etc.
Firmware improvements / speed to upgrade
More flexible remote configuration
Meters Continue to Evolve
PECO’s initial AMI meters were installed in 2012-2016
Sensus has introduced new functions over the years
  Enhanced Supervisory Messaging (ESM)
  Snapshot Data
  Firmware Upgrades/Enhancements
Changes driven by both the comms module and the meter
Aclara i210+c/DT-105
Sensus Stratus IQ/DT-96
A NextGen Meter is the newest type meter available for use at PECO. A key characteristic is its ability to support the V2 communications and its enhanced security measures.

## Slide 23: Next Gen AMI
New Meter Functions
  V2 Protocol
  More Data / Multiple Channels
  New Functions
      Distributed Intelligence / Grid Edge
      Loss of Neutral Detection
      Enhanced Temperature Sensing and Action
  Ultrasonic Gas Metering
      Remote Disconnect
      Pressure Sensing
Distributed Energy Resources – Solar, Batteries, etc
Electric Vehicles
    Load Disaggregation
    Charging Management

## Slide 27: Conclusion
Meter systems continue to evolve and increase functionality
NextGen Meters and AMI 2.0 are two similar manifestations of this evolution
Many of the initial deployments are nearing their useful end of life, leading to significant decisions by the AMI Operators

## Slide 28: Appendix

## Slide 29: PECO’s SGSM Team

## Slide 30: PECO F&MS and SGS
E05 Sr Maintenance Manager
E06 Director FMS and SGS
E05 Sr Manager SG Operations
E05 Sr Mgr SG Operatons
Administrative Assistant
Smart Meter Strategy & Distribution Automation
Data Analytics and Back Office operation
Field Operation

## Slide 31: PECO F&MS and SGS – SG Ops
E04 Mgr Analytics
E05 Sr Manager Advanced Grid Ops/Analytics
Glen Murphy
E04 Mgr SG Ops & Special Projects
1 Bus Analyst
2 Sr Quantitative Analyst
2 Sr Business Analyst
1 Assoc Business Analyst
1 AMI Ops Supervisor
2 Sr Business Analysts
E04 Principal Business Analyst
E04 Meter Maintenance Back Office
1 Sr. Business Analyst—Vendor Manager—N. Nayee
1 Sr. Contract Coordinator—TBD
1 Business Analyst—B. Enz
1 Assoc. Business Analyst —V. Elliot (4) Back office Contractors
(2) CCB Contractors until 6/2024
1 E02 Work Planner (Accenture) – A. Wilson
(14) Offshore Accenture Contractors
1 MM Back Office supervisor- N. Panetta
(4)- Business Analyst
(4) – Associate Business Analyst
(2) Long Term MM back-office Contractors
1 Rev Pro Back Office Supervisor- M. Salahuddin
(2) Business Analyst
(4) Associate Business Analyst
(2) U12
Luv Gera
Rasheeda Clark
Anthony Portelli
Lamar Ellis

## Slide 32: PECO F&MS and SGS – SG COE (Engineering)
E04 Mgr AMI
E05 Sr Manager Advanced Grid Ops
Glenn Pritchard
E04 Mgr Dist Automation
Quantitative Engineer
1 Network Engineer
1 AMI Endpoint Engineer
1 DA Endpoint engineer
1 Sawtooth Engineer
1 General Engineer (Meter Standards)
1 Sup Work Management
3 Engineering Tech Specialists
3 DA Ops Engineers
Sr RF Engineering Tech
OT SGP Program (Contractors)
Nate Nichols
Marc Bourrie
Open

## Slide 33: PECO F&MS and SGS – Meter Maint
E05 Sr. Meter Maintenance Manager
Mickey Bracey
E04 Revenue Protection Manager
Keith Steger
E03 Supervisor Rev Pro and HB
1 Work Planner — T. Mont
Open
E04 Meter Maintenance Manager Field
Harry Sheneman
E03 Supervisor Meter Shop and Electric MM 1 Work Planner — P. Morroney
Shawn Carbone
E03 Supervisor Gas MM
1 Work Planner — V. Stetler
Brendan Ryan
Administrative Coordinator
Darlene Banks